## Slide 1: Exploring Nuclear Energy

## Slide 2: Two Ways Nuclei Release Energy
Nuclear Fusion
Small nuclei combined to form one large nucleus
Requires immense amounts of energy to start and sustain
Process in the core of stars
Currently only a laboratory process
Nuclear Fission
Large nuclei split into smaller nuclei
Requires a critical mass to sustain the reaction
Process used in Naval vessels as well as nuclear power plants
Power plants use U-235
Iron is the “dead end” of both fusion and fission. As the lowest energy nucleus, it cannot be split nor fused.
Notes: These are the two nuclear processes from which we get vast amounts of energy.
Nuclear fusion is the process that powers our sun and other stars (see Solar 101 Long)
Nuclear fission is the process of splitting large atoms into smaller pieces. Lise Meitner, exiled from Germany in the late 1930s, corresponded with her colleague, Otto Hahn, about work they had started at the Planck Institute. Hahn was bombarding large nuclei with neutrons, attempting to make them even larger, but was getting what he thought were contaminants – atoms of much smaller mass than uranium. Eventually Meitner realized what was happening, and after doing calculations confirmed that the atoms were indeed being split, and the energy released was the amount of mass loss in the process according to Einstein’s equation, E=mc2.
Only certain isotopes are fissile, meaning able to be split. Uranium ore is high in U-238, which is not fissile; however, it does contain U-235, which is fissile. The ore goes through a series of chemical reactions and spinning in a centrifuge to enrich the uranium. Uranium must be at least 4% U-235 to sustain a nuclear fission reaction. Concentrations lower than this do not have the critical mass necessary to maintain fission. The enrichment process is stopped at 4% for nuclear fuel, or is allowed to continue to nearly 100% for weapons-grade plutonium using the same facility and processes.
The two nuclear weapons deployed in World War II used fission. Little Boy contained U-235 while Fat Man contained Plutonium-239. The two weapons used two different mechanical methods for achieving critical mass and initiating the uncontrolled, destructive reaction. Modern nuclear weapons are fusion bombs (a.k.a. “H-bombs”) that use fission to initiate the fusion reaction between hydrogen atoms. These weapons are orders of magnitude more powerful.
The nuclear fuel in a power plant can never explode like a nuclear weapon. It is not of high enough concentration. That’s not to say it cannot trigger a chemical reaction – just not a nuclear weapon-type reaction.

## Slide 3: Nuclear Fission Up Close and Personal
Uranium-235
Uranium-235
Barium-140
Krypton-93
Rubidium-92
Cesium-140
Neutron
Neutron
Neutron
Neutron
Neutron
Neutron
Gamma Radiation
Gamma Radiation
Notes: We often characterize U-235 as releasing 2 neutrons and forming Cs-140 and Rb-92. The fact is there are several different product scenarios that release 2, 3, or even 4 neutrons. It just depends on the incoming neutron impacts the uranium nucleus. Regardless, the neutrons ejected in the process then impact other uranium nuclei, triggering more reactions, and so on. Each fission releases energy in the form of gamma radiation, which heats up the water in the reactor core. Control rods are used in nuclear power plants to absorb some of the neutrons when the reaction needs to be slowed but not stopped.

## Slide 4: Global Energy Consumption, 2024
Data Source: EIA
Chart: Global Primary Energy Consumption by Source, 2024
| Coal | Natural gas | Petroleum | Nuclear | Renewables and other
 | 179.654 | 155.451 | 201.323 | 28.386 | 42.664
Chart: Global Electricity Generation by Source, 2024
| Fossil fuels | Hydropower | Nuclear | Wind | Solar | Biomass and waste | Geothermal | Tide and Wave
 | 18000 | 4513 | 2735 | 2512 | 2090 | 753 | 91 | 0.9
Notes: Since the Fukushima Daiichi accident in 2009, world nuclear power production has gone down. In 2009, 13.1% of electricity worldwide was produced by nuclear power. In 2011 that number had dropped to 10.8%.

## Slide 5: History of Global Nuclear Energy
Chart: World Total Generation from Nuclear, 1980-2023
| 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
 | 684.3802 | 778.6419 | 866.9867 | 982.4926 | 1197.8461 | 1426.4752 | 1518.7697 | 1655.3061 | 1796.1017 | 1844.5626 | 1910.12 | 1997.9042 | 2016.9766 | 2082.9954 | 2126.5506 | 2211.4302 | 2292.987 | 2272.7307 | 2317.467 | 2394.2321 | 2451.3963 | 2518.2787 | 2547.167 | 2519.2683 | 2620.4405 | 2626.5451 | 2661.3128 | 2609.6243 | 2598.8695 | 2561.7036 | 2629.1039 | 2518.0975 | 2347.0947 | 2364.2961 | 2419.5967 | 2448.1674 | 2488.9863 | 2517.0924 | 2570.0849 | 2668.7645 | 2595.7652 | 2698.3362 | 2588.8603 | 2665.785
Data Source: EIA
Fukushima disaster in Japan
Chernobyl disaster in Belarus

## Slide 6: Top Nuclear Generating Countries, 2023
Country | Nuclear Generation (BkWh) | Nuclear as percent of Total Generation
United States | 775 | 18.20%
China | 433 | 4.68%
France | 321 | 63.91%
Russia | 217 | 19.31%
South Korea | 180 | 30.33%
Country | Nuclear as percent of Total Generation
France | 63.91%
Slovakia | 63.65%
Ukraine | 50.64%
Hungary | 44.25%
Finland | 41.81%
Data Source: EIA

## Slide 8: US Electricity Generation by Source, 2024
Data Source: EIA
Chart: 
| Coal | Natural Gas | Nuclear | Petroleum | Other Gases (fossil fuels) | Hydroelectric | Biomass | Wind | Geothermal | Solar
 | 652.76 | 1864.874 | 781.979 | 15.267 | 9.807 | 236.326 | 46.741 | 456.454 | 15.671 | 218.538

## Slide 9: Nuclear Power Plant Locations
Image source: Nuclear Energy Institute
Notes: 28 states have at least one nuclear power plant.
Reactors 3 and 4 at the Vogtle generating station in Georgia were scheduled to come online in 2016, but that has been pushed back several times for the last several years. Reactor 3 started commercial operation in 2023. Reactor 4 has had hot testing nor has begun generating electricity.

## Slide 10: Top Ten States for Nuclear Generation by Percent of Total, 2024
44.8%
43.5%
39.7%
38.1%
32.0%
Data Source: EIA
Chart: Thousand Megawatt-hours
| New Hampshire | South Carolina | Illinois | New Jersey | Tennessee | Maryland | Connecticut | Georgia | North Carolina | Alabama
Nuclear | 9677 | 53770 | 99212 | 27677 | 32186 | 14767 | 16870 | 47976 | 43349 | 44487
All Other Sources | 7621 | 46610 | 86880 | 33555 | 43240 | 21048 | 28289 | 92505 | 92251 | 98732
US Total – 18.6%
57.94%
54.64%
44.09%
47.79%
41.62%
34.22%
54.86%
32.90%
32.47%
32.30%
Notes: This bar graph looks a little messy, but it is in order from bottom to top of most electricity generated as a percentage of the total in 2023. New Hampshire generates the greatest percentage of its electricity from nuclear energy, but Illinois generates the greatest number of thousand-megawatt-hours from nuclear power.

## Slide 11: Anatomy of a Nuclear Power Plant
Image Source: NRC
Notes: The pressurized water reactor (PWR) is the most common type of commercial reactor design used worldwide. It has primary, secondary, and external heat exchange systems and is pressurized to prevent water from boiling in the reactor.
Pressurized steam is piped into the reactor. Fission is taking place in the fuel rods within this reactor. The steam passing through the reactor is super heated.
The super heated pressurized steam then travels to the steam generator to heat a secondary water system.
The steam produced there travels through a steam line to the turbine to turn the generator and create electricity.
Unused steam continues to a condenser where water from the environment condenses it back into liquid water. The cooling water in the environment never comes into contact with the steam so it is safe to return to the environment. The newly condensed water can be pumped back into the containment building and reheated in the steam generator to start the process over again.
The pressurized steam loops back from the steam generator to the reactor to be super heated again.

## Slide 12: Anatomy of a Nuclear Power Plant
Image Source: NRC
Notes: A Boiling Water Reactor (BWR) is less common. In this design there is only one loop for the water to travel from the reactor to the turbine, whereas with the PWR there is a secondary loop.
In this model, water is pumped into the reactor creating steam and hot water that will turn the turbine attached to the generator to generate electricity. The unused steam/water mixture travels to the condenser and is condensed by water from the environment. The cooling water in the environment never comes into contact with the steam so it is safe to return to the environment. The resulting water in the condenser is pumped back into the reactor vessel to begin the process again.
Few nuclear power plants use the boiling-water design.

## Slide 13: Advantages of Nuclear Power
No Air Pollution from Generation
No Carbon Emissions from Generation
High Energy Density in Uranium
Operating Cost is Low After Construction
One fuel pellet = 1 ton coal
Image Source: Wikimedia Commons
Notes: The fuel pellets in the photograph are about 1 cm in diameter. Each has the ability to generate the same amount of electricity as 1 ton of coal.

## Slide 14: Drawbacks to Using Nuclear Power
Initial Construction Costs
Radioactive Waste Byproduct
Storage of Waste Byproduct
Natural Disasters Pose Threat
Public Perception
Image Source: NRC
Dry cask storage of radioactive waste at Diablo Canyon
Notes: There have been three large-scale nuclear accidents in the history of global nuclear power. Two were from mechanical or human failures and one, in Fukushima, Japan, was from a natural disaster.
The first was Three Mile Island, in 1979, in Pennsylvania.
The second was Chernobyl in 1986, in Bellarus.
The third was Fukushima in 2009, in Japan.

## Slide 15: US Nuclear Power Projects
Vogtle Power Station – Waynesboro, GA
Largest nuclear power plant in the United States
Reactor 1 – 1987; Reactor 2 – 1989; Reactor 3 – 2023; Reactor 4 – 2024
First new nuclear reactors built in the US in 30+ years
Crane Clean Energy Center (FKA Three Mile Island) – Middletown, PA
Three Mile Island was decommissioned in 2019
Constellation now owns the site
Reopening as early as 2027
Power Microsoft data centers
Palisades Nuclear Plant – Covert, MI
Shut down in 2022
Purchased by Holtec
In operational status, undergoing final inspections, expected to generate in 2026
Terrapower Natrium – Kemmerer, WY
Natrium reactor – sodium metal cooled fast reactor – 345 MW
Built on site of former coal plant
Includes molten salt energy storage for additional generation – increase to 500 MW
Construction permit approved in 2026
First ever non-light-water reactor permitted by NRC
Image source: Georgia Power
Image source: Constellation
Image source: Holtec
Image source: Terrapower

## Slide 16: Where Do We Go From Here?
Advanced Nuclear Reactor Designs
Molten Salt Reactors
Metal Cooled Reactor
Compact Fast Reactor
Small Modular Reactors
Fuel Design Developments
High-Assay Low-Enriched Uranium
Thorium
Tri-structural Isotropic Particles (TRISO)

## Slide 17: Advanced Reactor Designs
Molten Salt Reactor
Fuel can be incorporated into the coolant
Fuel can fission more completely
Metal Cooled Reactor
Similar to molten salt reactor
Fuel incorporated in coolant
Compact Fast Reactor
Allow for faster-moving neutrons
Combined with MSR or MCR, scaled down for use in remote areas
Small Modular Reactor
Safe operation at higher temperature
Passive safety designs
Molten salts are highly corrosive
Fuel can fission more completely
Safe operation at higher temperature
Passive safety designs
Sodium (common) is corrosive
Coolant is opaque
Do not require moderators to slow neutrons
Allows for economy of scale
Allows for “right now” power plant sizing
Allows for scaled up generation in future
“Plug and play” of nuclear power
Light-water reactors with ceramic pellet fuel
Can be combined with other advanced reactor designs

## Slide 18: Fuel Design Developments
LEU
HALEU
Thorium
TRISO
Low-enriched uranium, our current nuclear fuel
Ceramic pellet
Requires moderator
High-assay low-enriched uranium
5-20% U-235
Allows smaller reactor
Longer service period for fuel
Can be used in fast reactors and advanced designs
Th-232 is not fissile, but fertile
U-235 starts; emits neutrons that Th-232 uses to transmute into U-233
More complete fuel consumption
Less radioactive waste
Poppyseed-sized UO2 and UCO pellets covered with 4 layers of carbon and ceramics
Fuel is fully encapsulated
Can not melt down
Can be suspended in molten salt and metlal cooled reactor coolants
Extend service period because they react more completely and efficiently
3-5% U-235
Image source: Idaho National Laboratory

## Slide 19: What About Fusion?
So-called “cold fusion” from 1989 was not, in fact, fusion
DOE’s National Ignition Facility at Lawrence Livermore National Laboratory uses 192 laser beams aligning on a pea-sized target
December 2022, at LLNL, a fusion reaction produced more energy than was required to initiate the fusion reaction; this only accounts for the energy within the lasers, not the energy needed to form the laser beams themselves
Image Source: LLNL
Notes: The photograph is of the preamplifier chamber at the National Ignition Facility at LLNL. It increases the energy of the lasers before they reach the target chamber.
The fusion reaction referenced in December, 2022 was the first ever to achieve net energy. CNBC Article: https://www.cnbc.com/2022/12/13/nuclear-fusion-passes-major-milestone-net-energy.html

## Slide 20: Cherenkov Radiation

## Slide 21: When Things Go Wrong
Three Mile Island
Pressurized Water Reactors
Cooling malfunction caused part of the core in Reactor 2 to melt.
Some radioactive gas was released; health studies indicated it was not enough to cause adverse health effects.
Chernobyl
Engineers were testing low power threshold of reactor Number Four.
Reactor went out of control.
Resulting excessive heat generated hydrogen gas, led to an explosion and breach of the reactor building.
Fukushima
Earthquake with magnitude 9.0 led to a tsunami near the east coast of Honshu, the main island of Japan.
The tsunami overwhelmed the power plant, which is situated on the shoreline, and power went out.
Backup generators were in the lower levels of the power plant, and these were lost when the lower level was flooded.
The loss of backup power led to overheating and partial meltdown in three of the four reactors. Chemical explosions soon followed which breached the reactor buildings and allowed radioactive material to escape.

## Slide 22: Nuclear Power Plant Simulation
Image Source: NRC
Notes: Recall how Pressurized Boiler Reactors are laid out, with three loops – the reactor vessel loop (red), the steam loop (green), and the cooling loop (blue). The simulation is a walk-through of these three loops, with chips representing energy.

## Slide 23: Nuclear Power Plant Simulation
Notes: The three loops are represented in this diagram of the simulation, with the same colors as on the previous slide. Walk participants through the simulation, explaining that the little numbers on the diagram represent the number of energy chips each person should be holding at each point. Note that no one should ever have zero energy chips!