## Slide 1: Hydrogen
A Fuel for Today and Tomorrow

## Slide 2: Hydrogen is a Unique Energy Source
Element #1 on the periodic table
Diatomic molecule (H2) - 2 protons, 2 electrons
Highest energy content by WEIGHT, lowest by VOLUME
Most abundant element in the universe
Abundant on earth, but only bound to other elements

## Slide 3: Why Hydrogen?
It’s abundant, clean, efficient, and can be derived from diverse domestic resources.
HIGH EFFICIENCY & RELIABILITY
ZERO/NEAR ZERO EMISSIONS
.
Transportation
Distributed Generation
Biomass
Hydro
Wind
Solar
Geothermal
Coal
Nuclear
Natural Gas
Oil
With Carbon Sequestration

## Slide 4: Hydrogen is an Energy Carrier
Energy carriers move energy in a usable form from one place to another.
Electricity is an energy carrier; so are gasoline and hydrogen
Hydrogen allows us to store energy from many sources and bring it to where we need it.
Energy
Hydrogen

## Slide 5: Hydrogen is a Versatile Energy Source
Transportation Fuel
  Improved range compared to plug-in electric
  Internal combustion engines
  Applicable to most modes of transportation
Buildings
  Combined heat and power generation (CHP)
  Fuel cells – backup and primary power
Industry
  Hydrogen important in chemical processes
  Additional revenue stream opportunities

## Slide 6: Sources of Hydrogen
Hydrogen is not found on Earth in pure elemental form
Hydrogen is most prevalently bonded to oxygen and carbon
Water, natural gas, and crude oil are great sources of hydrogen
H
H
H
H
C

## Slide 7
Hydrogen Production Methods
Image credit: Department of Energy, Office of Energy Efficiency and Renewable Energy

## Slide 8: Steam Methane Reforming (SMR)
Steam-methane Reforming Reaction
Thermal Energy + CH4 (g) + H2O (g)  3 H2 (g) + CO (g)
Water-gas Shift Reaction
CO (g) + H2O (g)  CO2 (g) + H2 (g) + Thermal Energy

## Slide 9: Anatomy of a Fuel Cell
Image credit: FuelEconomy.gov
Anode: Site of oxidation – electrons removed from hydrogen, form H+
PEM: Proton Exchange Membrane – only allows H+ through
Cathode: Site of reduction – electrons rejoin H+ and combine with O2 to form H2O

## Slide 10: Hydrogen Fuel Cells Are Ideal for Transportation
Comparatively low operating temperature (80 °C)
  80 °C is a low temperature for fuel cell operation
  Low temperature limits CHP applications compared to other fuel cell types
  Quick startup, lower thermal stresses
Efficient at low loads (typical operating region for vehicles)

## Slide 11: Hydrogen Fuel Cell Vehicles
Electric Motor
Fuel Cell Stack
Battery
Hydrogen Tank

## Slide 12: Challenges of Hydrogen
Infrastructure – lack of fuel availability prevents widespread use of FCEV’s; lack of FCEV purchases prevents development of infrastructure
Storage – to achieve 300+ mile range, little cargo space in vehicle (energy density)
Fuel Cell Life – PEM fuel cells in vehicles last about 4,000 hours
Perceived Safety – compared to gasoline, hydrogen is safer, but misconceptions persist

## Slide 13: Current Hydrogen Fuel Use for Transportation in the U.S.
39 fueling stations
- 35 in California, 2 in South Carolina, and 2 in the Northeast
Fewer than 10 hydrogen fuel cell vehicles purchased each year
Three different FCEV models for 2017
  Honda Clarity
  Toyota Mirai
  Hyundai Tucson
  Down from six in 2016

## Slide 14: Hydrogen Storage
High-pressure storage tanks
  Tanks must be very strong.
  Tank size to achieve 300+ mile vehicle range is prohibitively large
Liquid hydrogen
  Higher density
  Very low temperature (about -253° C)
Metal hydrides
  Hydrogen combines chemically with some metals
  More efficient storage than high-pressure tanks
Carbon nanotubes
  Microscopic tubes of carbon, 2 nm in diameter
  Store hydrogen in their microscopic pores

## Slide 15: Hydrogen Storage
Hydrogen storage takes place…
  On-board a vehicle
  At production sites, in transit, and at refueling stations
Hydrogen can be stored in its pure form, or can be reformed on board a vehicle from other fuels

## Slide 16: Fuel Cell Life
While fuel cells do wear out over time, A PEM fuel cell in a vehicle should have a 4,000 hour service life, while stationary applications should last 40,000 hours.

## Slide 17: Hydrogen Flammability
Hydrogen Gasoline
Three Seconds
One minute
A fuel leak from a HCFEV would place the flame above the vehicle, whereas a gasoline leak places the flame below the vehicle.
Image from Washington State University, 2017

## Slide 18: So – why hydrogen?
Energy security
    Diverse domestic sources
    Flexibility of system
Economic security
    International leadership in technical
    development and deployment
    Price stability
Environmental security
    Potential to meet GHG targets
    Urban air quality improvements
    Reduction in air pollutants

## Slide 19: The NEED Project acknowledges…
Catherine E. Grégoire Padró
Los Alamos National Laboratory
Dr. Rajat K. Sen, Patty Kappaz
Sentech, Inc.

## Slide 20: For More Information
The NEED Project
  www.need.org
  info@need.org
  1-800-875-5029
Energy Information Administration
  U.S. Department of Energy
  www.eia.gov

## Slide 21: NEED IS SOCIAL!
Stay up-to-date with NEED. “Like” us on Facebook! Search for The NEED Project, and check out all we’ve got going on!
Follow us on Twitter. We share the latest energy news from around the country, @NEED_Project.
Follow us on Instagram and check out the photos taken at NEED events, instagram.com/theneedproject.
Follow us on Pinterest and pin ideas to use in your classroom, Pinterest.com/NeedProject.
Hydrogen 2018 ©The NEED Project